结构尺寸及主要技术参数

0.6/1kV单芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 1×1.5 1.38 0.8 1.4 5.8 56 - 12.1 - 3.5 1×2.5 1.78 0.8 1.4 6.2 69 54 7.41 12.1 1×4 2.25 1.0 1.4 7.0 94 70 4.61 7.41 1×6 2.76 1.0 1.4 7.6 119 82 3.08 4.61 1×10 4.1 1.0 1.4 8.9 173 111 1.83 3.08 1×16 5.1 1.0 1.4 9.9 239 140 1.15 0.91 1×25 6.4 1.2 1.5 11.8 357 200 0.727 1.20 1×35 7.6 1.2 1.5 13.0 461 243 0.524 0.868 1×50 8.9 1.4 1.6 14.9 614 318 0.387 0.641 1×70 10.7 1.4 1.6 16.7 834 407 0.268 0.443 1×95 12.6 1.6 1.7 19.2 1132 539 0.193 0.320 1×120 14.2 1.6 1.7 20.8 1384 636 0.153 0.253 1×120* 12.9 1.6 1.7 19.5 1334 604 0.153 0.253 1×150 15.8 1.8 1.7 22.8 1679 760 0.124 0.206 1×150* 14.5 1.8 1.7 21.5 1653 736 0.124 0.206 1×185 17.6 2.0 1.7 25.0 2065 912 0.0991 0.164 1×185* 16.0 2.0 1.7 23.4 1949 855 0.0991 0.164 1×240 20.3 2.2 1.7 28.1 2663 1149 0.0754 0.125 1×240* 18.3 2.2 1.7 26.1 2505 1073 0.0754 0.125 1×300 22.7 2.4 1.7 30.9 3296 1397 0.0601 0.100 1×300* 20.5 2.4 1.7 28.7 3162 1324 0.0601 0.100 1×400 25.7 2.6 1.7 34.3 4155 1725 0.0470 0.0778 1×400* 23.5 2.6 1.7 32.1 4046 1659 0.0470 0.0778 1×500 28.8 2.8 1.8 38.0 5192 2129 0.0366 0.0605 1×500* 26.5 2.8 1.8 35.7 5136 2074 0.0366 0.0605 1×630 32.5 2.8 1.9 41.9 6480 2596 0.0283 0.0469 1×630* 29.9 2.8 1.9 39.3 6337 2510 0.0283 0.0469 1×800 36.5 2.8 2.0 45.1 8091 3172 0.0221 0.0367 注:表示紧压圆形胶合导体

0.6/1kV单芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Testvoltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 2×1.5 1.38 0.8 1.8 10.4 109 - 12.1 - 3.5 2×2.5 1.78 0.8 1.8 11.2 137 106 7.41 12.1 2×4 2.25 1.0 1.8 12.9 192 142 4.61 7.41 2×6 2.76 1.0 1.8 13.9 224 170 3.08 4.61 2×10 4.1 1.0 1.8 16.9 362 235 1.83 3.08 2×16 5.1 1.0 1.8 18.6 505 303 1.15 0.91 2×25 6.4 1.2 1.8 22.0 748 429 0.727 1.20 2×35 7.6 1.2 1.8 24.3 971 528 0.524 0.868 2×50** 5.6 1.4 1.8 21.2 1120 559 0.387 0.641 2×70** 3.7 1.4 1.9 23.6 1555 745 0.268 0.443 2×95** 8.1 1.6 2.0 27.8 2112 988 0.193 0.320 2×120** 9.0 1.6 2.1 29.8 2596 1179 0.153 0.253 2×150** 11.7 1.8 2.2 36.2 3220 1471 0.124 0.206 2×185** 12.0 2.0 2.4 38.0 3946 1759 0.0991 0.164 2×240** 18.3 2.2 2.6 51.8 5501 2595 0.0754 0.125 2×300** 20.5 2.4 2.7 57.2 6951 3219 0.0601 0.100 注:表示紧压圆形胶合导体

0.6/1kV单芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 3×1.5 1.38 0.8 1.8 10.8 132 - 12.0 - 3.5 3×2.5 1.78 0.8 1.8 11.7 171 125 7.41 12.1 3×4 2.25 1.0 1.8 13.5 244 17 4.61 7.41 3×6 2.76 1.0 1.8 14.7 318 206 3.08 4.61 3×10 4.1 1.0 1.8 17.4 479 289 1.83 3.08 3×16 5.1 1.0 1.8 19.7 680 378 1.15 0.91 3×25 6.4 1.2 1.8 23.4 1021 542 0.727 1.20 3×35 7.6 1.2 1.8 25.9 1337 673 0.524 0.868 3×50* 6.8 1.4 1.8 25.5 1634 793 0.387 0.641 3×70* 8.0 1.4 1.9 28.0 2272 1058 0.268 0.443 3×95* 9.5 1.6 2.0 32.2 3113 1428 0.193 0.320 3×120* 10.4 1.6 2.2 35.9 3844 1719 0.153 0.253 3×150* 12.0 1.8 2.2 40.0 4735 2113 0.124 0.206 3×185* 13.2 2.0 2.4 44.1 5879 2598 0.0991 0.164 3×240* 14.9 2.2 2.5 49.0 7629 3317 0.0754 0.125 3×300* 16.9 2.4 2.6 52.5 9502 4092 0.0601 0.100 3×400* 19.2 2.6 2.8 59.2 12773 5504 0.0407 0.0778 注:表示紧压圆形胶合导体

0.6/1kV单芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 4×1.5 1.38 0.8 1.8 11.6 160 - 12.1 - 3.5 4×2.5 1.78 0.8 1.8 12.6 211 149 7.41 12.1 4×4 2.25 1.0 1.8 14.7 304 206 4.61 7.41 4×6 2.76 1.0 1.8 15.9 400 250 3.08 4.61 4×10 4.1 1.0 1.8 19.0 609 355 1.83 3.08 4×16 5.1 1.0 1.8 21.1 871 468 1.15 0.91 4×25 6.4 1.2 1.8 25.7 1316 678 0.727 1.20 4×35 7.6 1.2 1.8 28.5 1732 846 0.524 0.868 4×50* 7.4 1.4 1.9 28.3 2160 1040 0.387 0.641 4×70* 8.7 1.4 1.9 31.7 3029 1411 0.268 0.443 4×95* 10.8 1.6 2.2 38.7 4126 1880 0.193 0.320 4×120* 11.7 1.6 2.4 42.2 5104 2271 0.153 0.253 4×150* 13.1 1.8 2.5 47.9 6266 2770 0.124 0.206 4×185* 14.7 2.0 2.5 53.3 7763 3388 0.0991 0.164 4×240* 16.8 2.2 2.8 58.3 10046 4296 0.0754 0.125 4×300* 18.6 2.4 3.0 62.3 12523 5310 0.0601 0.100 4×400* 21.7 2.6 3.1 64.6 16851 7159 0.0470 0.0778 注:表示紧压圆形胶合导体

0.6/1kV,3+1芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 芯数 No.of 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 Cores mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 3×1.5+1×1.0 3 1.38 0.8 1.8 11.4 153 - 12.1 - 3.5 1 1.13 0.8 18.1 - 3×2.5+1.5 3 1.78 0.8 1.8 12.3 198 - 7.41 - 1 1.38 0.8 12.1 - 3×4+1×2.5 3 2.25 1.0 1.8 14.1 280 191 4.61 7.41 1 1.78 0.8 7.41 12.1 3×6+1×4 3 2.76 1.0 1.8 15.6 375 238 3.08 4.61 1 2.25 1.0 4.61 7.41 3×10+1×6 3 4.1 1.0 1.8 18.2 555 327 1.83 3.08 1 2.76 1.0 3.08 4.61 3×16+1×10 3 5.1 1.0 1.8 20.9 804 438 1.15 1.91 1 4.1 1.0 1.83 3.08 3×25+1×16 3 6.4 1.2 1.8 24.6 1202 622 0.727 1.20 1 5.1 1.0 1.15 1.91 3×35+1×16 3 7.6 1.2 1.8 26.7 1511 746 0.524 0.868 1 5.1 1.0 1.15 1.91 3×50+1×25 3* 7.5 1.4 1.9 28.3 1973 972 0.387 0.641 1* 6.4 1.2 0.727 1.20 3×70+1×35 3* 8.6 1.4 2.0 32.3 2721 1286 0.268 0.443 1* 7.6 1.2 0.524 0.868 3×95+1×50 3* 10.8 1.6 2.1 36.7 3699 1715 0.193 0.320 1* 8.9 1.4 0.387 0.641 3×120+1×70 3* 11.7 1.6 2.3 40.3 4661 2102 0.153 0.253 1* 10.7 1.4 0.268 0.443 3×150+1×70 3* 13.1 1.8 2.4 46.1 5567 2512 0.124 0.206 1* 10.7 1.4 0.268 0.443 3×185+1×95 3* 14.7 2.0 2.6 49.8 6979 3098 0.991 0.164 1* 12.6 1.6 0.193 0.320 3×240+1×120 3* 16.8 2.2 2.7 54.6 8957 3886 0.0754 0.125 1* 14.2 1.6 0.153 0.253 3×300+1×150 3* 18.6 2.4 2.9 58.9 11149 4807 0.0601 0.100 1* 15.8 1.8 0.124 0.206 3×400+1×185 3* 21.7 2.6 3.2 66.9 14559 6181 0.0470 0.0778 1* 17.6 2.0 0.0991 0.164 注:表示紧压扇形导体

0.6/1kV单芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 5×1.5 1.38 0.8 1.8 12.4 189 - 12.1 - 3.5 5×2.5 1.78 0.8 1.8 13.5 251 174 7.41 12.1 5×4 2.25 1.0 1.8 15.8 366 243 4.61 7.41 5×6 2.76 1.0 1.8 17.3 484 297 3.08 4.61 5×10 4.1 1.0 1.8 20.7 742 425 1.83 3.08 5×16 5.1 1.0 1.8 23.6 1068 564 1.15 1.91 5×25 6.4 1.2 1.8 28.2 1619 821 0.727 1.20 5×35 7.6 1.2 1.9 31.5 2150 1043 0.524 0.868 5×50 8.9 1.4 2.0 36.4 2889 1391 0.387 0.641 5×50* 8.3 1.4 2.0 34.8 2788 1329 0.387 0.641 5×70 10.7 1.4 2.2 42.1 4051 1886 0.268 0.443 5×70* 9.8 1.4 2.2 39.6 3829 1767 0.268 0.443 5×95 12.6 1.6 2.4 48.7 5553 2551 0.193 0.320 5×95* 11.5 1.6 2.4 45.7 5339 2415 0.193 0.320 5×120 14.2 1.6 2.5 53.2 6866 3071 0.153 0.253 5×120* 12.9 1.6 2.5 49.7 6602 2904 0.153 0.253 5×150 15.8 1.8 2.7 58.8 8434 3772 0.124 0.206 5×150* 14.5 1.8 2.7 55.5 8283 3634 0.124 0.206 5×185 17.6 2.0 2.9 65.4 10500 4653 0.0991 0.164 5×185* 16.0 2.0 2.9 61.0 9715 4165 0.0991 0.164 5×240 20.3 2.2 3.1 74.0 13663 5978 0.0754 0.125 5×240* 18.3 2.2 3.1 68.7 12813 5547 0.0754 0.125 5×300 22.7 2.4 3.3 82.0 17027 7386 0.0601 0.100 5×300* 20.5 2.4 3.3 76.1 16278 6948 0.0601 0.100 5×400 25.7 2.6 3.7 91.9 21658 9327 0.0470 0.0778 5×400* 23.5 2.6 3.7 86.1 21017 8903 0.0470 0.0778 注:表示紧压圆形胶合导体

0.6/1kV,4+1芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 芯数 No.of 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 Cores mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 4×1.5+1×1.0 4 1.38 0.8 1.8 12.3 183 - 12.0 - 3.5 1 1.13 0.8 18.1 - 4×2.5+1.5 4 1.78 0.8 1.8 13.3 239 - 7.41 - 1 1.38 0.8 12.1 - 4×4+1×2.5 4 2.25 1.0 1.8 15.4 343 229 4.61 7.41 1 1.78 0.8 7.41 12.1 4×6+1×4 4 2.76 1.0 1.8 17.0 460 286 3.08 4.61 1 2.25 1.0 4.61 7.41 4×10+1×6 4 4.1 1.0 1.8 20.0 690 399 1.83 3.08 1 2.76 1.0 3.08 4.61 4×16+1×10 4 5.1 1.0 1.8 23.0 1002 535 1.15 1.91 1 4.1 1.0 1.83 3.08 4×25+1×16 4 6.4 1.2 1.8 27.3 1508 768 0.727 1.20 1 5.1 1.0 1.15 1.91 4×35+1×16 4 7.6 1.2 1.8 29.7 1919 932 0.524 0.868 1 5.1 1.0 1.15 1.91 4×50+1×25 4* 8.3 1.4 2.0 33.7 2554 1235 0.387 0.641 1* 6.4 1.2 0.727 1.20 4×70+1×35 4* 9.8 1.4 2.1 37.7 3465 1601 0.268 0.443 1* 7.6 1.2 0.524 0.868 4×95+1×50 4* 11.5 1.6 2.3 43.5 4817 2186 0.193 0.320 1* 8.9 1.4 0.387 0.641 4×120+1×70 4* 12.9 1.6 2.5 47.8 6053 2682 0.153 0.253 1* 10.7 1.4 0.268 0.443 4×150+1×70 4* 14.5 1.8 2.6 52.3 7375 3244 0.124 0.206 1* 10.7 1.4 0.268 0.443 4×185+1×95 4* 16.0 2.0 2.8 57.9 8955 3930 0.991 0.164 1* 12.6 1.6 0.193 0.320 4×240+1×120 4* 18.3 2.2 3.0 64.9 11547 4995 0.0754 0.125 1* 14.2 1.6 0.153 0.253 4×300+1×150 4* 20.5 2.4 3.2 72.0 14652 6258 0.0601 0.100 1* 15.8 1.8 0.124 0.206 4×400+1×185 4* 23.5 2.6 3.5 81.0 18734 7933 0.0470 0.0778 1* 17.6 2.0 0.0991 0.164 注:表示紧压扇形导体

0.6/1kV,3+2芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 芯数 No.of 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 Cores mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 3×1.5+2×1.0 3 1.38 0.8 1.8 12.2 176 - 12.1 - 3.5 2 1.13 0.8 18.1 - 3×2.5+2×1.5 3 1.78 0.8 1.8 13.1 226 - 7.41 - 2 1.38 0.8 12.1 - 3×4+2×2.5 3 2.25 1.0 1.8 14.9 320 215 4.61 7.41 2 1.78 0.8 7.41 12.1 3×6+2×4 3 2.76 1.0 1.8 16.7 437 276 3.08 4.61 2 2.25 1.0 4.61 7.41 3×10+2×6 3 4.1 1.0 1.8 19.3 637 373 1.83 3.08 2 2.76 1.0 3.08 4.61 3×16+2×10 3 5.1 1.0 1.8 22.4 937 507 1.15 1.91 2 4.1 1.0 1.83 3.08 3×25+2×16 3 6.4 1.2 1.8 26.4 1397 716 0.727 1.20 2 5.1 1.0 1.15 1.91 3×35+2×16 3 7.6 1.2 1.8 28.2 1703 838 0.524 0.868 2 5.1 1.0 1.15 1.91 3×50+2×25 3** 7.4 1.4 1.9 31.7 2280 1100 0.387 0.641 2 6.4 1.2 0.727 1.20 3×70+2×35 3** 8.7 1.4 2.1 36.0 3122 1453 0.268 0.443 2 7.6 1.2 0.524 0.868 3×95+2×50 3** 10.8 1.6 2.2 41.4 4300 1962 0.193 0.320 2 8.9 1.4 0.387 0.641 3×120+2×70 3* 12.9 1.6 2.4 45.7 5486 2443 0.153 0.253 2 10.7 1.4 0.268 0.443 3×150+2×70 3* 14.5 1.8 2.5 49.1 6476 2862 0.124 0.206 2 10.7 1.4 0.268 0.443 3×185+2×95 3* 16.0 2.0 2.7 54.9 8034 3535 0.991 0.164 2 12.6 1.6 0.193 0.320 3×240+2×120 3* 18.3 2.2 2.9 61.2 10293 4455 0.0754 0.125 2 14.2 1.6 0.153 0.253 3×300+2×150 3* 20.5 2.4 3.1 67.9 13039 5581 0.0601 0.100 2 15.8 1.8 0.124 0.206 3×400+2×185 3* 23.5 2.6 3.3 75.9 16474 6985 0.0470 0.0778 2 17.6 2.0 0.0991 0.164 注:表示紧压扇形导体

0.6/1kV单芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 1×10 4.1 1.0 1.8 12.3 253 191 1.83 3.08 3.5 1×16 5.1 1.0 1.8 13.3 328 229 1.15 1.91 1×25 6.4 1.2 1.8 15.0 453 296 0.727 1.20 1×35 7.6 1.2 1.8 16.2 565 347 0.524 0.868 1×50 8.9 1.4 1.8 17.9 723 427 0.387 0.641 1×70 10.7 1.4 1.8 19.7 956 530 0.268 0.443 1×95 12.6 1.6 1.8 22.0 1260 667 0.193 0.320 1×120 14.2 1.6 1.8 23.6 1523 774 0.153 0.253 1×120* 12.9 1.6 1.8 22.3 1464 735 0.153 0.253 1×150 15.8 1.8 1.8 25.6 1831 912 0.124 0.206 1×150* 14.5 1.8 1.8 24.3 1796 879 0.124 0.206 1×185 17.6 2.0 1.8 27.8 2233 1081 0.0991 0.164 1×185* 16.0 2.0 1.8 26.2 2107 1013 0.0991 0.164 1×240 20.3 2.2 1.8 30.9 2851 1337 0.0754 0.125 1×240* 18.3 2.2 1.8 28.9 2680 1249 0.0754 0.125 1×300 22.7 2.4 2.0 34.7 3570 1670 0.0601 0.100 1×300* 20.5 2.4 2.0 33.7 3695 1857 0.0601 0.100 1×400 25.7 2.6 2.1 39.5 4803 2373 0.0470 0.0778 1×400* 23.5 2.6 2.1 37.3 4655 2268 0.0470 0.0778 1×500 28.8 2.8 2.2 43.2 5903 2840 0.0366 0.0605 1×500* 26.5 2.8 2.2 40.9 5806 2744 0.0366 0.0605 1×630 32.5 2.8 2.3 47.1 7254 3371 0.0283 0.0469 1×630* 29.9 2.8 2.3 44.5 7065 3238 0.0283 0.0469 1×800 36.5 2.8 2.4 51.3 8935 4017 0.0221 0.0367 注:表示紧压圆形胶合导体

0.6/1kV二芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 2×4 2.25 1.0 1.8 14.7 304 255 4.61 7.41 3.5 2×6 2.76 1.0 1.8 15.7 367 292 3.08 4.61 2×10 4.1 1.0 1.8 18.3 495 368 1.83 3.08 2×16 5.1 1.0 1.8 20.4 655 454 1.15 1.91 2×25 6.4 1.2 1.8 23.8 929 610 0.727 1.20 2×35 7.6 1.2 1.8 26.1 1172 729 0.524 0.868 2×50** 5.6 1.4 1.8 23.0 1293 733 0.387 0.641 2×70** 6.7 1.4 2.0 27.4 1999 1190 0.268 0.443 2×95** 8.1 1.6 2.1 31.2 2627 1504 0.193 0.320 2×120** 9.0 1.6 2.2 33.2 3147 1731 0.153 0.253 2×150** 11.7 1.8 2.3 39.6 3891 2143 0.124 0.206 2×185** 12.0 2.0 2.5 41.4 4645 2458 0.0991 0.164 2×240* 18.3 2.2 2.7 55.2 6460 3554 0.0754 0.125 2×300* 20.5 2.4 2.8 60.6 8011 4279 0.0601 0.100 注:表示紧压圆形胶合导体

0.6/1kV二芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 3×4 2.25 1.0 1.8 15.3 363 289 4.61 7.41 3.5 3×6 2.76 1.0 1.8 16.5 447 335 3.08 4.61 3×10 4.1 1.0 1.8 19.2 620 429 1.83 3.08 3×16 5.1 1.0 1.8 21.5 840 538 1.15 1.91 3×25 6.4 1.2 1.8 25.2 1213 734 0.727 1.20 3×35 7.6 1.2 1.8 27.7 1551 887 0.524 0.868 3×50* 7.0 1.4 1.8 27.3 1844 1004 0.387 0.641 3×70* 8.0 1.4 2.0 30.4 2818 1604 0.268 0.443 3×95* 9.5 1.6 2.1 34.8 3741 2056 0.193 0.320 3×120* 10.4 1.6 2.2 38.3 4521 2396 0.153 0.253 3×150* 12.0 1.8 2.3 41.4 5489 2866 0.124 0.206 3×185* 13.2 2.0 2.5 45.3 6702 3412 0.0991 0.164 3×240* 14.9 2.2 2.6 50.2 8555 4243 0.0754 0.125 3×300* 16.9 2.4 2.7 54.1 10524 5114 0.0601 0.100 3×400* 19.2 2.6 3.0 60.4 14053 6785 0.0470 0.0778 注:表示紧压扇形胶合导体

0.6/1kV四芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 4×4 2.25 1.0 1.8 16.5 434 336 4.61 7.41 3.5 4×6 2.76 1.0 1.8 17.7 542 392 3.08 4.61 4×10 4.1 1.0 1.8 20.8 764 510 1.83 3.08 4×16 5.1 1.0 1.8 23.4 1048 645 1.15 1.91 4×25 6.4 1.2 1.8 27.5 1529 891 0.727 1.20 4×35 7.6 1.2 1.8 30.3 1969 1048 0.524 0.868 4×50* 7.4 1.4 2.0 32.1 2703 1583 0.387 0.641 4×70* 8.7 1.4 2.1 35.7 3616 1999 0.268 0.443 4×95* 10.8 1.6 2.3 41.3 4845 2599 0.193 0.320 4×120* 11.7 1.6 2.4 45.4 5866 3032 0.153 0.253 4×150* 13.1 1.8 2.6 51.1 7124 3628 0.124 0.206 4×185* 14.7 2.0 2.8 56.3 8702 4327 0.0991 0.164 4×240* 16.8 2.2 2.9 60.9 11097 5347 0.0754 0.125 4×300* 18.6 2.4 3.1 66.1 13693 6480 0.0601 0.100 4×400* 21.7 2.6 3.2 71.4 18282 8590 0.0470 0.0778 注:表示紧压扇形胶合导

0.6/1kV,3+1芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV22 VLV22 VY23 VLY23）

导体标称截面 Nom.cross-sectionalarea of conductor 芯数 No.of 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 Cores mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 3×4+1×2.5 3 2.25 1.0 1.8 16.9 412 322 4.61 7.41 3.5 1 1.78 0.8 7.41 12.1 3×6+1×4 3 2.76 1.0 1.8 18.4 512 384 3.08 4.61 1 2.25 1.0 4.61 7.41 3×10+1×6 3 4.1 1.0 1.8 21.0 709 482 1.83 3.08 1 2.76 1.0 3.08 4.61 3×16+1×10 3 5.1 1.0 1.8 23.7 981 616 1.15 1.91 1 4.1 1.0 1.83 3.08 3×25+1×16 3 6.4 1.2 1.8 24.4 1412 833 0.727 1.20 1 5.1 1.0 1.15 1.91 3×35+1×16 3 7.6 1.2 1.8 29.5 1740 975 0.524 0.868 1 5.1 1.0 1.15 1.91 3×50+1×25 3* 7.5 1.4 1.9 30.9 2214 1215 0.387 0.641 1 6.4 1.2 0.727 1.20 3×70+1×35 3* 8.6 1.4 2.0 34.0 3329 1895 0.268 0.443 1 7.6 1.2 0.524 0.868 3×95+1×50 3* 10.8 1.69 2.2 39.3 4424 2440 0.193 0.320 1 8.9 1.4 0.387 0.641 3×120+1×70 3* 11.7 1.6 2.3 42.3 5448 2890 0.153 0.253 1 10.7 1.4 0.268 0.443 3×150+1×70 3* 13.1 1.8 2.5 46.8 6431 3376 0.124 0.206 1 10.7 1.4 0.268 0.443 3×185+1×95 4* 14.7 2.0 2.6 52.1 7902 4020 0.0991 0.164 1 12.6 1.6 0.193 0.420 3×240+1×120 3* 16.8 2.2 2.8 56.8 10013 4942 0.0754 0.120 1 14.2 1.6 0.153 0.253 3×300+1×150 3* 18.6 2.4 2.9 61.2 12325 5983 0.0601 0.100 1 15.8 1.8 0.124 0.206 3×400+1×185 3* 21.7 2.6 3.3 69.1 15890 7511 0.0470 0.0778 1 17.6 2.0 0.0991 0.164 注:表示紧压扇形导体

0.6/1kV四芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV VLV VY VLY）

导体标称截面 Nom.cross-sectionalarea of conductor 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 5×4 2.25 1.0 1.8 17.6 508 384 4.61 7.41 3.5 5×6 2.76 1.0 1.8 19.1 651 464 3.08 4.61 5×10 4.1 1.0 1.8 22.5 924 607 1.83 3.08 5×16 5.1 1.0 1.8 25.4 1276 772 1.15 1.91 5×25 6.4 1.2 1.8 30.0 1871 1073 0.727 1.20 5×35 7.6 1.2 2.0 32.2 2755 1649 0.524 0.868 5×50 8.9 1.4 2.1 40.2 3588 2089 0.387 0.641 5×50* 83. 1.4 2.1 38.6 3460 2001 0.387 0.641 5×70 10.7 1.4 2.3 45.5 4835 2669 0.268 0.443 5×70* 9.8 1.4 2.3 43.0 4566 2504 0.268 0.443 5×95 12.6 1.6 2.5 52.1 6459 3456 0.193 0.320 5×95* 11.5 1.6 2.5 49.1 6188 3264 0.193 0.320 5×120 14.2 1.6 2.6 56.6 7856 4062 0.153 0.253 5×120* 12.9 1.6 2.6 53.1 7524 3827 0.153 0.253 5×150 15.8 1.8 2.8 62.2 9528 4866 0.124 0.206 5×150* 14.5 1.8 2.8 58.9 9313 4663 0.124 0.206 5×185 17.6 2.0 2.9 68.6 11683 5836 0.0991 0.164 5×185* 14.5 2.0 2.9 60.2 10739 5189 0.0991 0.164 5×240 20.3 2.2 3.2 77.4 15034 7349 0.0754 0.125 5×240* 18.3 2.2 2.2 72.1 14083 6817 0.0754 0.125 5×300 22.7 2.4 3.4 85.4 18546 8906 0.0601 0.100 5×300* 20.5 2.4 3.4 79.5 17685 8356 0.0601 0.100 5×400 25.7 2.6 3.8 96.5 24194 11863 0.0470 0.0778 5×400* 23.5 2.6 3.8 90.7 23388 11274 0.0470 0.0778 注:表示紧压圆形胶合导

0.6/1kV,4+1芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV22 VLV22 VY23 VLY23）

导体标称截面 Nom.cross-sectionalarea of conductor 芯数 No.of 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 Cores mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 4×4+1×2.5 4 2.25 1.0 1.8 17.2 480 366 4.61 7.41 3.5 1 1.78 0.8 7.41 12.0 4×6+1×4 4 2.76 1.0 1.8 18.8 613 439 3.08 4.61 1 2.25 1.0 4.61 7.41 4×10+1×6 4 4.1 1.0 1.8 21.8 853 562 1.83 3.08 1 2.76 1.0 3.08 4.61 4×16+1×10 4 5.1 1.0 1.8 24.8 1191 724 1.15 1.91 1 4.1 1.0 1.83 3.08 4×25+1×16 4 6.4 1.2 1.8 29.1 1734 995 0.727 1.20 1 5.1 1.0 1.15 1.91 4×35+1×16 4 7.6 1.2 1.9 31.7 2180 1195 0.524 0.868 1 5.1 1.0 1.15 1.91 4×50+1×25 4* 8.3 1.4 2.0 36.9 3162 1843 0.387 0.641 1 6.5 1.2 0.727 1.20 4×70+1×35 4* 9.8 1.4 2.2 41.1 4168 2303 0.268 0.443 1 7.6 1.2 0.524 0.868 4×95+1×50 4* 11.5 1.69 2.4 46.9 5627 2996 0.193 0.320 1 8.9 1.4 0.387 0.641 4×120+1×70 4* 12.9 1.6 2.5 51.0 6917 3546 0.153 0.253 1 10.7 1.4 0.268 0.443 4×150+1×70 4* 14.5 1.8 2.7 55.7 8346 4214 0.124 0.206 1 10.7 1.4 0.268 0.443 4×185+1×95 4* 16.0 2.0 2.9 61.3 10026 5001 0.0991 0.164 1 17.6 1.6 0.193 0.420 4×240+1×120 4* 18.3 2.2 3.1 68.3 12747 6195 0.0754 0.120 1 14.2 1.6 0.153 0.253 4×300+1×150 4* 20.5 2.4 3.3 75.4 15983 7589 0.0601 0.100 1 15.8 1.8 0.124 0.206 4×400+1×185 4* 23.5 2.6 3.6 85.6 20968 10166 0.0470 0.0778 1 17.6 2.0 0.0991 0.164 注:表示紧压圆形导体

0.6/1kV,3+2芯聚氯绝缘单芯聚氯乙烯/聚乙烯护套电力电缆（VV22 VLV22 VY23 VLY23）

导体标称截面 Nom.cross-sectionalarea of conductor 芯数 No.of 导体直径 Diameter of conductor 绝缘厚度 Insulation thickness 护套厚度 Outer sheath thickness 电缆近似外径 Approx. overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c) mm2 Cores mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 3×4+2×2.5 3 2.25 1.0 1.8 16.7 452 347 4.61 7.41 3.5 2 1.78 0.8 7.41 12.1 3×6+2×4 3 2.76 1.0 1.8 18.5 586 425 3.08 4.61 2 2.25 1.0 4.61 7.41 3×10+2×6 3 4.1 1.0 1.8 21.1 795 530 1.83 3.08 2 2.76 1.0 3.08 4.61 3×16+2×10 3 5.1 1.0 1.8 24.2 1121 692 1.15 1.91 2 4.1 1.0 1.83 3.08 3×25+2×16 3 6.4 1.2 1.8 28.2 1615 934 0.727 1.20 2 5.1 1.0 1.15 1.91 3×35+2×16 3 7.6 1.2 1.8 30.0 1937 1072 0.524 0.868 2 5.1 1.0 1.15 1.91 3×50+2×25 3** 7.5 1.4 2.0 35.5 2888 1709 0.387 0.641 2 6.0 1.2 0.727 1.20 3×70+2×35 3** 8.6 1.4 2.1 39.2 3774 2105 0.268 0.443 1 7.0 1.2 0.524 0.868 3×95+2×50 3** 10.8 1.69 2.3 44.8 5071 2733 0.193 0.320 2 8.3 1.4 0.387 0.641 3×120+2×70 3** 12.9 1.6 2.5 49.1 6335 3292 0.153 0.253 2 10.7 1.4 0.268 0.443 3×150+2×70 3* 14.5 1.8 2.6 52.5 7388 3774 0.124 0.206 2 10.7 1.4 0.268 0.443 3×185+2×95 3* 16.0 2.0 2.8 58.3 9049 4550 0.0991 0.164 2 12.6 1.6 0.193 0.420 3×240+2×120 3* 18.3 2.2 3.0 64.6 11424 5585 0.0754 0.120 2 14.2 1.6 0.153 0.253 3×300+2×150 3* 20.5 2.4 3.2 71.3 14294 6836 0.0601 0.100 2 15.8 1.8 0.124 0.206 3×400+2×185 3* 23.5 2.6 3.4 79.3 17877 8388 0.0470 0.0778 2 17.6 2.0 0.0991 0.164 注:表示紧压圆形绞合导体 **表示紧压扇形导体

0.6/1kV二芯交联聚乙烯绝缘钢丝聚氯乙烯/聚乙烯护套电力电缆（YJV32 YJLV32 YJY33 YJLY33）

标称截面 Nominal cross-sectional area 导体直径 Diameter of conductor 绝缘厚度 Insulation thickess 护套厚度 Sheath thickess 电缆近似外径 Approx.overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c.) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 2×10 4.1 1.0 1.8 22.1 1020 892 1.83 3.08 3.5 2×16 5.1 1.0 1.8 24.2 1241 1040 1.15 1.91 2×25 6.4 1.2 1.8 27.6 1613 1294 0.727 1.20 2×35 7.6 1.2 1.9 30.1 1934 1492 0.524 0.868 2×50** 5.6 1.4 2.0 27.2 1977 1417 0.387 0.641 2×70** 6.7 1.4 2.1 30.8 2746 1937 0.268 0.443 2×95** 8.1 1.6 2.2 34.6 3475 2352 0.193 0.320 2×120** 9.0 1.6 2.3 37.6 4412 2995 0.153 0.253 2×150** 11.7 1.8 2.5 44.4 5445 3697 0.124 0.206 2×185** 12.0 2.0 2.6 46.2 6255 4068 0.0991 0.164 2×240* 18.3 2.2 2.8 60.2 8636 5730 0.0754 0.125 2×300* 20.5 2.4 3.0 66.0 10460 6728 0.0601 0.100 *表示紧压圆形绞合导体；**表示紧压扇形导体

0.6/1kV三芯交联聚乙烯绝缘钢丝铠装聚氯乙烯/聚乙烯护套电力电缆（YJV32 YJLV32 YJY33 YJLY33）

标称截面 Nominal cross-sectional area 导体直径 Diameter of conductor 绝缘厚度 Insulation thickess 护套厚度 Sheath thickess 电缆近似外径 Approx.overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c.) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 3×10 4.1 1.0 1.8 23.0 1172 981 1.83 3.08 3.5 3×16 5.1 1.0 1.8 25.3 1457 1155 1.15 1.19 3×25 6.4 1.2 1.8 29.0 1936 1458 0.727 1.20 3×35 7.6 1.2 1.9 31.7 2359 1695 0.524 0.868 3×50** 6.8 1.4 2.0 31.3 29.06 2065 0.387 0.641 3×70** 8.0 1.4 2.1 34.8 3727 2514 0.268 0.443 3×95** 9.5 1.6 2.2 39.0 5178 3494 0.193 0.320 3×120** 10.4 1.6 2.3 42.5 6087 3962 0.153 0.253 3×150** 12.0 1.8 2.5 48.2 7241 4619 0.124 0.206 3×185** 13.2 2.0 2.6 52.3 8620 5339 0.0991 0.164 3×240* 14.9 2.2 2.8 57.6 10720 6408 0.754 0.125 3×300* 16.9 2.4 2.9 61.1 12929 7519 0.0601 0.100 3×400* 19.2 2.6 3.2 69.7 17134 10865 0.0470 0.0778 *表示紧压扇形导体

0.6/1kV四芯交联聚乙烯绝缘钢丝铠装聚氯乙烯/聚乙烯护套电力电缆（YJV32 YJLV32 YJY33 YJLY33）

标称截面 Nominal cross-sectional area 导体直径 Diameter of conductor 绝缘厚度 Insulation thickess 护套厚度 Sheath thickess 电缆近似外径 Approx.overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c.) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 4×10 4.1 1.0 1.8 24.6 1362 1108 1.83 3.08 3.5 4×16 5.1 1.0 1.8 27.2 1719 1316 1.15 1.19 4×25 6.4 1.2 1.9 31.5 2333 1695 0.727 1.20 4×35 7.6 1.2 2.0 35.3 3145 2260 0.524 0.868 4×50* 7.5 1.4 2.1 35.1 3557 2437 0.387 0.641 4×70* 8.6 1.4 2.3 39.3 4607 2989 0.268 0.443 4×95* 10.8 1.6 2.5 46.9 6498 4252 0.193 0.320 4×120* 11.7 1.6 2.6 51.3 7674 4841 0.153 0.253 4×150* 13.1 1.8 2.8 57.1 9126 5630 0.124 0.206 4×185* 14.7 2.0 3.0 63.8 10895 6520 0.0991 0.164 4×240* 16.8 2.2 3.2 68.6 13562 7813 0.754 0.125 4×300* 18.6 2.4 3.3 72.6 17419 10206 0.0601 0.100 4×400* 21.7 2.6 3.5 78.3 22858 13167 0.0470 0.0778 *表示紧压扇形导体

0.6/1kV 3+1芯交联聚乙烯绝缘钢丝铠装聚氯乙烯/聚乙烯护套电力电缆（YJV32 YJLV32 YJY33 YJLY33）

标称截面 Nominal cross-sectional area 芯数 No.of Cores 导体直径 Diameter of conductor 绝缘厚度 Insulation thickess 护套厚度 Sheath thickess 电缆近似外径 Approx.overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c.) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 3×10+1×6 3 4.1 1.0 1.8 23.8 1276 1049 1.83 3.08 3.5 1 2.76 1.0 3.08 4.61 3×16+1×10 3 5.1 1.0 1.8 26.5 1625 1260 1.15 1.91 1 4.1 1.0 1.83 3.08 3×25+1×16 3 6.4 1.2 1.9 30.4 2177 1597 0.727 1.20 1 5.1 1.0 1.15 1.91 3×35+1×16 3 7.6 1.4 1.9 32.5 2564 1799 0.524 0.868 1 5.1 1.2 1.15 1.91 3×50+1×25 3* 7.5 1.4 2.1 35.1 3395 2395 0.387 0.641 1 6.4 1.2 0.727 1.20 3×70+1×35 3* 8.6 1.6 2.2 38.4 4385 2951 0.268 0.443 1 7.6 1.4 0.524 0.868 3×95+1×50 3* 10.8 1.6 2.4 43.7 5614 3630 0.193 0.320 1 8.9 1.4 0.387 0.641 3×120+1×70 3* 1.7 1.8 2.5 43.9 7320 4762 0.153 0.253 1 10.7 1.4 0.268 0.443 3×150+1×70 3* 13.1 2.0 2.7 51.7 8421 5366 0.124 0.206 1 10.7 1.6 0.264 0.443 3×185+1×95 3* 14.7 2.2 2.8 59.1 10144 6263 0.0991 0.164 1 12.6 1.6 0.193 0.320 3×240+1×120 3* 16.8 2.4 3.0 65.4 10524 7453 0.0754 0.125 1 14.2 1.8 0.153 0.253 3×300+1×150 3* 18.6 2.6 3.2 72.1 15148 8806 0.0601 0.100 1 15.8 2.0 0.124 0.206 3×400+1×185 3* 21.7 3.6 82.4 20463 12084 0.0470 0.0778 1 17.6 0.0991 0.164

0.6/1kV五芯交联聚乙烯绝缘钢丝铠装聚氯乙烯/聚乙烯护套电力电缆（YJV32 YJLV32 YJY33 YJLY33）

标称截面 Nominal cross-sectional area 导体直径 Diameter of conductor 绝缘厚度 Insulation thickess 护套厚度 Sheath thickess 电缆近似外径 Approx.overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c.) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 5×10 4.1 1.0 1.8 26.3 1559 1241 1.83 3.08 3.5 5×16 5.1 1.0 1.8 29.2 1989 1486 1.15 1.19 5×25 6.4 1.2 2.0 34.2 2745 1947 0.727 1.20 5×35 7.6 1.2 2.1 38.3 3697 2591 0.524 0.868 5×50 8.9 1.4 2.2 43.2 4661 3163 0.387 0.641 5×50* 8.3 1.4 2.2 41.6 4483 3025 0.387 0.641 5×0 10.7 1.4 2.5 50.3 6620 4455 0.268 0.443 5×70* 9.8 1.4 2.5 47.8 6255 4194 0.268 0.443 5×95 12.6 1.6 2.7 57.1 8529 5526 0.193 0.320 5×95* 11.5 1.6 2.7 54.1 8138 5214 0.193 0.320 5×120 14.2 1.6 2.8 61.8 10138 6344 0.153 0.253 5×120* 12.9 1.6 2.8 58.3 9663 5965 0.153 0.253 5×150 15.8 1.8 3.0 67.6 12065 7403 0.124 0.206 5×150* 14.5 1.8 3.0 64.3 11711 7062 0.124 0.206 5×185 17.6 2.0 3.2 74.4 14525 8678 0.0991 0.164 5×185* 14.5 2.0 3.2 70.0 13642 8092 0.0991 0.164 5×240 20.3 2.2 3.5 84.7 19380 11694 0.0754 0.125 5×240* 18.3 2.2 3.5 79.4 18132 10866 0.0754 0.125 5×300 22.7 2.4 3.7 92.9 23378 13737 0.0601 0.100 5×300* 20.5 2.4 3.7 87.0 22184 12854 0.0601 0.100 5×400 25.7 2.6 4.0 103.0 28783 16452 0.0470 0.0778 5×400* 23.5 2.6 4.0 97.2 27700 15586 0.0470 0.0778 *表示紧压圆形绞合导体

0.6/1kV，3+2芯交联聚乙烯绝缘钢丝铠装聚氯乙烯/聚乙烯护套电力电缆（YJV32 YJLV32 YJY33 YJLY33）

标称截面 Nominal cross-sectional area 芯数 No.of Cores 导体直径 Diameter of conductor 绝缘厚度 Insulation thickess 护套厚度 Sheath thickess 电缆近似外径 Approx.overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c.) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 3×10+2×6 3 4.1 1.0 1.8 24.9 1440 1175 1.83 3.08 3.5 2 2.76 1.0 3.08 4.61 3×16+2×10 3 5.1 1.0 1.8 28 1859 1430 1.15 1.91 2 4.1 1.0 1.83 3.08 3×25+2×16 3 6.4 1.2 1.9 32.2 2492 1812 0.727 1.20 2 5.1 1.0 1.15 1.91 3×35+2×16 3 7.6 1.2 2.0 34.2 2848 1983 0.524 0.868 2 5.1 1.0 1.15 1.91 3×50+2×25 3** 7.5 1.4 2.1 38.5 3916 2736 0.387 0.641 2 6.5 1.2 0.727 1.20 3×70+2×35 3** 8.6 1.4 2.3 42.8 4947 3279 0.268 0.443 2 7.6 1.2 0.524 0.868 3×95+2×50 3** 10.8 1.6 2.5 48.8 6953 4615 0.193 0.320 2 8.9 1.4 0.387 0.641 3×120+2×70 3* 12.9 1.6 2.6 53.2 8433 5390 0.153 0.253 2 10.7 1.4 0.268 0.443 3×150+2×70 3* 14.5 1.8 2.8 55.4 9671 6057 0.124 0.206 2 10.7 1.4 0.268 0.443 3×185+2×95 3* 16.0 2.0 3.0 63.1 11588 7089 0.0991 0.164 2 12.6 1.6 0.193 0.320 3×240+2×120 3* 18.3 2.2 3.2 69.3 14277 8439 0.075 0.125 2 14.2 1.6 0.153 0.253 3×300+2×150 3* 20.5 2.4 3.4 76.2 18561 11103 0.0601 0.100 2 15.8 1.8 0.124 0.206 3×400+2×185 3* 23.5 2.6 3.7 86.8 22702 13213 0.0470 0.0778 2 17.6 2.0 0.0991 0.164 *表示紧压圆形绞合导体；**表示紧压扇形导体。

0.6/1kV,4+1芯交联聚乙烯绝缘钢丝铠装聚氯乙烯/聚乙烯护套电力电缆（YJV32 YJLV32 YJY33 YJLY33）

标称截面 Nominal cross-sectional area 芯数 No.of Cores 导体直径 Diameter of conductor 绝缘厚度 Insulation thickess 护套厚度 Sheath thickess 电缆近似外径 Approx.overall diameter of cable 电缆近似重量 Approx.weight of cable kg/km 20℃导体最大直流电阻 Max.d.c resistance of conductor(20℃)Ω/km 试验电压 Test voltage(a.c.) mm2 mm mm mm mm 铜芯 铝芯 铜芯 铝芯 KV/5min 4×10+1×6 4 4.1 1.0 1.8 25.6 1513 1222 1.83 3.08 3.5 1 2.76 1.0 3.08 4.61 4×16+1×10 4 5.1 1.0 1.8 28.6 1944 1478 1.15 1.91 1 4.1 1.0 1.83 3.08 4×25+1×16 4 6.4 1.2 1.9 33.1 2643 1904 0.727 1.20 1 5.1 1.0 1.15 1.91 4×35+1×16 4 7.6 1.2 2.1 36.7 3475 2489 0.524 0.868 1 5.1 1.0 1.15 1.91 4×50+1×25 4* 7.5 1.4 2.2 40.5 4287 2968 0.387 0.641 1 6.5 1.2 0.727 1.20 4×70+1×35 4* 8.6 1.4 2.3 44.5 5384 3519 0.268 0.443 1 7.6 1.2 0.524 0.868 4×95+1×50 4* 10.8 1.6 2.6 51.7 7619 4988 0.193 0.320 1 8.9 1.4 0.387 0.641 4×120+1×70 4* 12.9 1.6 2.7 56.0 9103 5733 0.153 0.253 1 10.7 1.4 0.268 0.443 4×150+1×70 4* 14.5 1.8 2.9 60.9 10772 6641 0.124 0.206 1 10.7 1.4 0.268 0.443 4×185+1×95 4* 16.0 2.0 3.1 66.7 12710 7685 0.0991 0.164 1 12.6 1.6 0.193 0.320 4×240+1×120 4* 18.3 2.2 3.3 75.2 16801 10249 0.075 0.125 1 14.2 1.6 0.153 0.253 4×300+1×150 4* 20.5 2.4 3.6 82.9 20560 12166 0.0601 0.100 1 15.8 1.8 0.124 0.206 4×400+1×185 4* 23.5 2.6 3.9 92.1 25403 14601 0.0470 0.0778 1 17.6 2.0 0.0991 0.164 *表示紧压圆形绞合导体。

在空气中

导体 Conductor 导体标称截面 Nom.cross- sectional areaof conductor 无铠装电缆 Unarmored cable 铠装电缆 Armored cable mm2 单芯 Singe-core 二芯 2-core 三芯 3-core 五芯 5-core 单芯 Singe-core 二芯 2-core 三芯 3-core 五芯 5-core 四芯 4-core 四芯 4-core 铜导体 Copper conductor 1.5 20 23 17 15 16 - - - - - 2.5 26 29 23 19 20 - - - - - 4 34 38 32 26 27 - - 33 27 28 6 43 49 38 32 42 - - 39 33 34 10 59 67 53 46 47 59 67 54 47 48 16 77 88 71 60 61 77 88 73 61 62 25 98 111 90 77 79 98 111 92 79 79 35 124 140 110 95 97 124 140 113 97 97 50 148 168 135 115 117 148 168 137 117 119 70 188 214 165 145 148 188 214 169 148 151 95 230 260 211 185 189 230 260 215 189 192 120 267 303 245 211 215 267 303 251 214 218 150 307 349 280 245 251 307 349 285 250 252 185 353 400 320 280 285 353 400 326 284 287 240 418 475 - 335 342 418 475 - 341 346 300 480 545 - 375 383 480 545 - 382 387 400 567 642 - - - 567 642 - - - 500 656 745 - - - 656 745 - - - 630 755 856 - - - 755 856 - - - 800 871 987 - - - 871 987 - - - 铝导体 Aluminium conductor 2.5 20 23 18 15 15 - - - - - 4 26 30 24 20 20 - - 24 20 20 6 35 39 32 26 27 - - 32 26 27 10 45 51 42 35 36 45 51 42 35 36 16 60 68 55 47 48 60 68 55 47 48 25 78 89 70 60 61 78 89 70 60 61 35 94 107 86 74 76 94 107 86 74 76 50 115 131 105 90 92 115 131 105 90 92 70 144 163 131 115 117 144 163 131 115 117 95 177 200 165 140 143 177 200 165 140 143 120 205 233 161 165 169 205 233 191 165 169 150 238 271 215 191 194 238 271 215 191 194 185 275 311 251 215 219 275 311 251 215 219 240 324 367 - 260 265 324 367 - 260 265 300 373 423 - 295 301 373 423 - 295 301 400 443 503 - - - 443 503 - - - 500 518 586 - - - 518 586 - - - 630 607 688 - - - 607 688 - - - 800 706 800 - - - 706 800 - - -

在土壤中

导体 Conductor 导体标称截面 Nom.cross- sectional areaof conductor 无铠装电缆 Unarmored cable 铠装电缆 Armored cable mm2 单芯 Singe-core 二芯 2-core 三芯 3-core 五芯 5-core 单芯 Singe-core 二芯 2-core 三芯 3-core 五芯 5-core 四芯 4-core 四芯 4-core 铜导体 Copper conductor 1.5 24 27 26 22 22 - - - - - 2.5 31 35 34 29 30 - - - - - 4 40 46 44 38 39 - - 44 38 39 6 50 57 56 47 48 - - 56 47 48 10 68 77 76 65 66 68 77 76 65 66 16 86 98 100 84 86 86 98 100 84 86 25 111 126 125 110 112 111 126 125 110 112 35 131 149 155 130 133 131 149 155 130 133 50 160 181 185 155 158 160 181 185 155 158 70 197 223 230 195 199 197 223 230 195 199 95 234 265 275 230 235 234 265 275 230 235 120 267 302 310 260 265 267 302 310 260 265 150 299 339 350 300 306 299 339 350 300 306 185 340 386 395 335 341 340 386 395 335 341 240 394 446 - 390 398 394 446 - 390 398 300 447 507 - 435 444 447 507 - 435 444 400 513 581 - - - 513 581 - - - 500 582 660 - - - 582 660 - - - 630 664 753 - - - 664 753 - - - 800 746 846 - - - 746 846 - - - 铝导体 Aluminium conductor 2.5 25 28 26 23 23 - - - - - 4 32 36 35 30 31 - - 35 30 31 6 41 47 45 39 40 - - 45 39 40 10 52 60 59 50 51 52 60 59 50 51 16 68 77 77 65 66 68 77 77 65 66 25 86 98 100 84 85 86 98 100 84 85 35 103 116 120 100 102 103 116 120 100 102 50 123 140 145 120 122 123 140 145 120 122 70 152 172 175 150 153 152 172 175 150 153 95 180 205 210 185 189 180 205 210 185 189 120 205 233 245 205 209 205 233 245 205 209 150 234 265 275 230 235 234 265 275 230 235 185 262 298 310 260 265 262 298 310 260 265 240 308 349 - 300 306 308 349 - 300 306 300 349 395 - 340 347 349 395 340 347 400 402 456 - - - 402 456 - - 500 459 521 - - - 459 521 - - 630 529 560 - - - 529 560 - - 800 603 684 - - - 603 684 - -